## Slide 1: Velociraptor (Th): Critical Design Review
Project Manager/Systems Engineer:
Paul Ahumada
E&C Engineer: Kevin Armentrout
M&D Engineer: Victoria Osaji

## Slide 2: Project Objectives
The Velociraptor resembles a Theropoda
The robot is a toy
The Velociraptor is due by December 15, 2016
The Velociraptor will use a 3DoT Board
The Velociraptor will be controlled by Arxterra Control Panel
The Velociraptor will play in a game

## Slide 3: Mission Profile
3rd Generation Velociraptor is a robot developed by the CSULB 2016 Fall Semester class that will compete in a Jurassic/Modern Game: Save The Human with other toys on the last day of class, December 15, 2016. The game will involve Velociraptor chasing another robot through various terrain by tele-robotic communication on the Arxterra Control Panel. The arena and terrain the Velociraptor must traverse is developed by the Game Committee. The mission will display the robotic applications of the 3DoT Board developed by Arxterra and Velociraptor’s movement capabilities. – PM Paul Ahumada

## Slide 4: The Design

## Slide 5: Project Features
IMU Sensor
3DoT Board
UCI Linkages

## Slide 6: Experiments
What has been done
Servo Simulations
Motor Torque Simulations
Command Data Processing for Motors
I2C communication for IMU and Accuracy Test
What needs to be done
Motor shaft indicators
Jitter Test – Test for noise
Functional Test of Raptor’s Static Walking FSM
Functional Test of Raptor’s Dynamic Walking Algorithm
Precision Testing of I2C ADC and Motor Shaft Position
Precision Testing of Head/Tail Servo
Precision Testing of Platform Servo
Test of Battery’s Longevity During Normal Operation

## Slide 7: System Block Diagram

## Slide 8: Interface Matrix

## Slide 9: Cable Tree
Wire Gauge for External PCB to 3DoT board battery is minimum AWG 20
Other wire gauges are minimum size AWG 24
Wire’s will be in Cable mesh similar to a sleeve that is flexible
Approximate length’s 3-6 inches

## Slide 10: Software Block Diagram

## Slide 11: Arxterra Control Panel

## Slide 12: Command Decoding

## Slide 13: Components: Motor: GM9 Right Angle Gear Box
Motor Selection was based off of two requirements, static / walking that for a peak torque of 140 mN-m.
The GM-9 Right Angle Motor was the Superior candidate in all considerable factors:
  Speed: 40 RPM
  No Load Current:
    55 mA (Peak, Tested)
  Stall Current
    461 mA (Peak, Tested)
  Average Current
    151 mA (Simulated)
  Stall Torque: 311 mN-m
  Weight: 33g (Each)

## Slide 14: Components: IMU: MPU 6050
IMU Selection was based off IMU sensitivity and Accuracy, and I2C compatibility.
The MPU 6050 was one of two I2C IMUs, but the only IMU with accuracy to the Hundredth of a degree.
Blogpost:
IMU Testing |  |  | 
Test | X | Y | Z
Steady State | 0.113° (MAE) | 0.02° (MAE) | 0.13%
6 Degree Decline | 0.54° (MAE) | 2.60% | 0.13%
6 Degree Incline | 0.69° (MAE) | 0.65% | 0.14%
20 Degree Roll Left | 0.67% | 0.58° (MAE) | 1.14%
20 Degree Roll Right | 1.13% | 0.40° (MAE) | 1.67%

## Slide 15: Components: Servos: SG-90
Servo Selection was based off of the requirement for 1 degree precision and the following torque requirements:
  Head and Tail Servo: 18-45mN-m
  Platform Servo: 105-232 mN-m
An additional requirement for the servo was to have the size of the servo as small as possible for component size minimization and weight reduction.
The SG 90 covers both of these requirements, and is in the Micro servo class.
The SG90 has an additional, distinct advantage: it is free, allowing us to meet our budget.

## Slide 16: Components: Rotary Encoder: Bourne 3382 and A/D: ADS-1015
Traditional Rotary encoders could not be used on this project due to encoder accuracy and the requirement for external interrupts to time the Encoders.
  Rotary Encoders that use 2 Bit Grey code have a positional sensitivity of 30 degrees. This does not meet the required accuracy for our project.
The Bourne 3382 uses a continuous motion potentiometer to provide an output that is proportional to shaft position.
  Limits of this design are:
    A dead band from 330-360 degrees.
    Noise from 3.3v Line
    A/D Accuracy
The ADS-1115 provides I2C A/D conversion with 12 bit accuracy.
Sensitivity at 3.3v:
  0.81 mV
Sensitivity of Shaft Indication:
  0.088 Degrees

## Slide 17: Firmware: 3DoT Library Communication
Communication between the Robot and the operator will occur via Bluetooth using the Arxterra Control Panel.
Custom Commands that will be implemented are:
  Move
  Static/Dynamic Motion Control
Custom Telemetry that will be Implemented:
  X, Y, and Z IMU angles
  Servo and Leg Position

## Slide 20: Electronics: Shield Fritz

## Slide 21: Electronics: Breadboard and 3DoT Trace Cutting

## Slide 22: Electronics: PCB Electrical Schematic

## Slide 23
Mechanical Subsystem: PCB Layout

## Slide 24
Mechanical Subsystem Hardware Design

## Slide 25
Mechanical Subsystem Design

## Slide 26
Subsystem Design and Unique Tasks (Planned)
Static Test
Static: A way to assess the contact and connections between parts

## Slide 27: Verification & Validation Test Strategy
Verification tests primary purpose is to show results from quantifiable research and experiments done on level 2 requirements
Validation determines whether the Velociraptor accomplished its job as a toy to be enjoyed in a game like setting

## Slide 28: Verification Overview
Objective: Static versus Dynamic Walking Control
Requirement: Shall have a dynamic walking mode to utilize platform servo. Otherwise, platform servo shall not be used.
Success Criteria: Boolean value for dynamic walking 'on' should have platform servo correct tilted robot. Dynamic walking mode 'off' should have platform servo not react to a tilted robot
Validation Method: Demonstration
Objective: Power
Requirement: Shall use external battery to power external devices on 3DoT board. The battery shall deliver a minimum of 1563 mA-Hours for external devices during normal operation.
Success Criteria: The external devices will be able be powered under normal operation for minimum one hour.
Validation Method: Analysis
Objective: Power
Requirement: External PCB shall be powered by [3.3V (I2C interface) or external Battery connection]. The power shall not exceed rating of [LDO 3.3V – other devices].
Success Criteria: Boolean value for dynamic walking 'on' should have platform servo correct tilted robot. Dynamic walking mode 'off' should have platform servo not react to a tilted robot
Validation Method: Analysis

## Slide 29: Verification Overview
Objective: Movement
Requirement: The CoG on axis of legs shall be controlled by one servo. The velocity of the CoG of the head and tail shall not exceed [TBD] m/s in order to avoid momentum tip over the robot.
Success Criteria: The H/T servo will not cause the robot to tip over during static movement.
Validation Method: Demonstration
Objective: Movement
Requirement: Shall use two DC motors to operate legs at optimal torque [TBD] rated for 50% margin of mass driven.
Success Criteria: Weight will be added to the robot to be at 150% of mass while it walks. The motors should not stall while walking.
Validation Method: Demonstration
Objective: Power
Requirement: Implement Rotary Sensor that shall track cyclical motion at precision of 1 degree.
Success Criteria: The Arduino program will Serial.write outputs of potentiometer sensors data at predetermined angles.
Validation Method: Demonstration

## Slide 30: Validation Overview
Objective: Game Participation
Requirement: The 3rd Generation Velociraptor shall participate in the Game: Save The Human proposed by the game committee
Success Criteria: The Velociraptor will operate in the game by going through uneven surfaces, hills, and turning and be considered a fun toy.
Validation Method: Demonstration
Objective: Appearance
Requirement: The Velociraptor shall resemble a T-Rex of the Theropodous Dinosaur Suborder
Success Criteria: The robot undergoes a visual test to see if it resembles a Velociraptor
Validation Method: Inspection
Objective: Budget
Requirement: 3rd Generation Velociraptor budget shall not cost more than $150.00. This estimate is based upon Customer and Project Team agreement on October 7th, 2016.
Success Criteria: Documentation of the product must not exceed $150.00
Validation Method: Inspection

## Slide 34: Updated Schedule/Critical Path

## Slide 35
Chart: Project Burn Down and Percent Completion 8/25 - 12/15
| 42607 | 42614 | 42621 | 42628 | 42635 | 42642 | 42649 | 42656 | 42663 | 42670 | 42677 | 42684 | 42691 | 42698 | 42705 | 42712 | 42719
Schedule of Tasks | 44 | 44 | 42 | 41 | 40 | 37 | 31 | 17 | 16 | 8 | 6 | 5 | 4 | 4 | 2 | 0 | 0
Tasks To Do | 44 | 44 | 43 | 42 | 41 | 39 | 35 | 30 | 27 | 25 | 18
% Completion | 0 | 0 | 1.1364 | 2.2727 | 3.4091 | 5.6818 | 10.2273 | 15.9091 | 19.3182 | 21.5909 | 29.5455

## Slide 36: Sources
Arxterra Blog Posts
Verification and Validation Matrix
Resource Reports