## Slide 1: Velociraptor Fall 2016
Project Manager – Paul Ahumada
E&C – Kevin Armentrout
Systems Engineer– Robert Licari
Manufacturering Engineer– Vickie Osaji

## Slide 2: Mission Profile
3rd Generation Velociraptor is a robot developed by the CSULB 2016 Fall Semester class that will expand on previous semester’s designs. The Velociraptor is to be a toy resembling Theropoda dinosaurs. Velociraptor shall compete in a Jurassic/Modern Game: Save The Human with other toys on the last day of class, December 15, 2016. The game will involve Velociraptor chasing another robot through various terrain by tele-robotic communication on the Arxterra Control Panel. The arena the Velociraptor must traverse is developed by the Game Committee and customer. The mission will display the robotic applications of the 3DoT Board developed by Arxterra and Velociraptor’s movement capabilities. – PM Paul Ahumada

## Slide 3: Mission Profile
The mission statement as described by University of Connecticut (UCONN)
Velociraptor shall participate in a game by the end of Fall 2016 Semester

## Slide 4: Program Objectives
The Velociraptor is a dinosaur toy
The Velociraptor is on a deadline
The Velociraptor will use a 3DoT board
The Velociraptor will be controlled by an Arxterra Control Panel
The Velociraptor will play in a game

## Slide 5: Dinosaur Toy
Represents a dinosaur of the Theropodous Suborder classification
Little arms, big legs
Should be portable

## Slide 6: Time Limit
Last Day of Class is December 15, 2016

## Slide 7: 3DoT Board
Show capabilities in any robot
Provide actuators to robot

## Slide 8: Arxterra Control Panel
Send commands to 3DoT board via Bluetooth
Telemetry

## Slide 9: Participate in a Game
Game: Save The Human
Projects participating
Goliath
Velociraptors
Biped

## Slide 10: Challenges of the Game
Slopes
Uneven surfaces
Time Limit
Field of View
Making Contact
Biped becoming invincible

## Slide 11: Arena Layout

## Slide 12: Level 1 Program Requirements
The 3rd Generation Velociraptor shall participate in the Game: Save The Human proposed by the game committee
3rd Generation Velociraptor budget shall not cost more than $400.00. This estimate is based upon 2nd and 1st Generation Bipeds and the Cost Resource Report
The Velociraptor shall demonstrate its capabilities on December 15, 2016 according to CSULB Calendar 2016-2017

## Slide 13: Level 1 Project Requirements
The Velociraptor shall resemble a T-Rex of the Theropodous Dinosaur Suborder
The Velociraptor shall navigate through the game terrain provided by the game committee. Velociraptor shall:
  Navigate on incline/declines no greater than 6.5 degrees
  Shall navigate on uneven surface heights no larger than .5 cm
  Shall utilize a foot design capable of traction on all surfaces of game
  Battery shall provide sufficient power to robot for duration of the game
The Velociraptor shall statically walk on a flat surface
The Velociraptor shall dynamically walk on all surfaces of the game
The Velociraptor shall use Bluetooth to communicate with Arxterra Control Panel
The Velociraptor shall use a 3DoT board and implement I2C
The Velociraptor shall use a Portable Power Source

## Slide 14: Design Creativity and/or Innovation
Creative solutions did not yield results we had hoped for
Brainstorming created results we wanted
  Inverted Pendulum by platform design - CoG change on axis of Head and Tail
  Toe articulation for uneven surfaces
  Keep rigid body structure of neck and tail

## Slide 15: Level 2 Requirements

## Slide 16
Shall implement a control system PID which shifts center of gravity (CoG) on axis of legs to maintain stability. (Level 1-2,3,4)
  This shall be performed by one servo.
  Verification shall be performed via basic walking test when initial prototype has been created
Shall implement a control system PID which shifts CoG on axis of head, body, and tail to maintain stability. (Level 1-2,4)
  This shall be performed by a single servo controlling a platform.
  Verification shall be performed via basic walking test when initial prototype has been created.

## Slide 17
3. Shall have two leg mechanism, modeled after UCI linkages, supporting mass of robot with 50% margin. (Level 1-1)
  Verification shall be derived from Total Mass goal is ~657g; therefore, legs shall be able to support 985.5g.
4.Shall use leg UCI linkage design that operates with cyclical movement that shall be controlled by DC motors. (Level 1-1)
  Verification shall be performed via basic walking test when initial prototype has been created.
  [Encoder/Hall Effect] will be utilized to track cyclical motion at [TBD] rev/min.

## Slide 18
5. Shall implement a control system PID which shifts the CoG over the planted leg while statically walking. (Level 1-3)
  Mechanically this will be implemented by the movement of the head and tail.
  Verification shall be performed via basic walking test when initial prototype has been created.
6. Arduino Microcontroller 3DoT shall implement control algorithms for stability and user control. (Level 1-4)
  Shall be able to maintain stability if user communication or power is lost.
  Shall be able to remain stable when reacting to an outside force of [TBD]
  Verification shall be done via a tilt test and a brownout/blackout test of communications and supply power.

## Slide 19
7. Shall utilize Bluetooth 4.0 BLE to provide Velociraptor commands via RC controls given by Arxterra Application. (Level 1-5,6)
  Bluetooth Communications shall be maintained up to 50m. (1)
  Shall be able to accept and perform a test command suite and report back telemetry including Motor Direction and Speed
  Verification shall be done at 50m Bluetooth range and will be given a simple gauntlet of test commands. Test will be deemed successful if raptor performs command and telemetry is reported successfully.

## Slide 20
8. Shall connect head and tail servo and platform via 3DoT Board interface (Level 1-6)
  Shall receive input voltage from [Directly from Battery or LDO]
  Shall not exceed a [Polyfuse [TBD] and [TBD] margin, via LDO constraint]
9. Inertial Measurement Unit (IMU) shall track acceleration, gyration, and magnetic force. (Level 1-5,6)
  Shall provide X, Y, and Z angles at [TBD] precision.
  Unit will be asked to record data at and during a 0 and 180 degree rotation about each axis.

## Slide 21
10. The robot shall have the ability to change direction to either the left or right. (Level 1-2)
  Shall be able to change direction in 360 degrees when stationary
  Turn Test will be used to verify this on approved game surfaces.
11. The robot shall be able to maintain stability by dynamic walking during course navigation and be able to traverse through terrain. (Level 1-2,3)
  IMU shall send data as inputs to control system for dynamic stability.
  An increasing incline test(incremented by 1 degree/test) shall be used to verify this.

## Slide 22
12. Shall use batteries for 3DoT board and custom PCB. (Level 1-7)
The robot shall be able to continuously operate in game arena for a minimum of one hour
  Verification for batteries and operation shall be done with a continuous movement test. Robot will be active with batteries at full charge and will run until robot ceases to walk normally.

## Slide 23: PBS

## Slide 24: System Block Diagram

## Slide 25: Interface Definitions

## Slide 26: Software Block Diagram

## Slide 27: Electronics and Control Subsystems

## Slide 28: Control Subsystem
Level II Requirements 1, 2, 5 and 8
In order to determine the amount of deviation of center of mass it was necessary to identify inertial moments of the Raptor.
Moments were calculated using the proposed mass for the head and tail units, roughly equivalent to two AA batteries to mirror previous raptor designs.
Radii of the head and tail were varied to illustrate the effect of changing the radius of the head and tail units.

## Slide 29: Control Subsystem
Dynamic Walking Requirement (Level 2-
Common servo speed varied between 80 and 130 RPM based off vendor specifications.
To illustrate the effect of torque on the body versus RPM, centripetal force calculations must be made:
Once centripetal force has been identified, centripetal torque is identified as:
Tip Over Torque = 162mN-m

## Slide 30: Control Subsystem
Iterative Design Problems Identification
Problem 1:
  DC Motors do not provide position indication, which would identify when to shift CoG.
Potential Solution 1a:
  Use Hall Effect Sensors on the shaft of the DC motor with permanent magnets to identify when the feet are on the ground.
Potential Solution 1b:
  Use a Rotary Encoder for precise measurement of shaft position.
Problem 2:
  Both the Rotary encoder and the Hall Effect Sensor requires additional I/O ports for each DC motor. The 3DoT board has limited I/O slots, and only I2C slots are available
Solution 2:
  Use an I2C I/O expander to allow for the use of additional digital inputs and outputs.
Trade-Off studies will need to be conducted to whether a Hall effect sensor or rotary encoder is desired for the project.
https://upload.wikimedia.org/wikipedia/commons/thumb/7/7e/Hall_sensor_tach.gif/220px-Hall_sensor_tach.gif

## Slide 31: Control Subsystem
Level II Requirements 6-8, 10 and 12
In order to adjust for the inclination of the raptor, the entire raptor must shift its alignment to adjust to the horizontal plane.
To accomplish this we need a servo to precisely control the horizontal plane position, and a sensor which will identify the inclination of the robot.
An IMU will be used to identify inclination and angular acceleration

## Slide 32: Control Subsystems
IMU Requirements (Level 2-9):
  Detect inclination angles of up to 6.5 degrees per the game’s rules
  This corresponds to the head and tail positions on the chart to the right. The maximum expected movement is about 1.1 cm

## Slide 33: Power Subsystem (Level 1-7)
System Engineering determined that the allocation of resources, in mA for the DC motors was an average current draw of 1500mA each, with 300mA average current for each servo.
Additionally, the game’s duration must be, at minimum, one hour long.
This requires batteries that have a combined rating at a minimum of 3700mA-h.
3DoT battery form factor limits on board battery selection, so any externally connected batteries must supply power via an external bus.
Systems Engineering Computed Allocation

## Slide 34: Power Subsystem
Boost Converter Bypass to External Power Rail
Grounding of External Power at 3DoT Common

## Slide 35: Power Subsystem
An externally fed motor driver allows for full current duty of the motor to be supplied by the external power source, leaving the entirety of the current allocation for the on board battery to the servos, the Leonardo, and the on-board Bluetooth.
All external I/O systems will be powered through the external power rail, including all I2C components. This leaves 710mA allocated to 3DoT components and servos.

## Slide 36: Power Subsystem
DC Motor Power Consumption analysis
  DC Motor Current Draw is entirely dependent on torque on the motor, and rated no and full load current values provided by the manufacturer.
  Calculating torque on the motor is incredibly complicated due to the multiple lever arms acting on the motor.
  Three primary lever arms are used for torque calculations.
  These calculations are not definitive, but explanatory to the approximate value of motor torque.

## Slide 37: Power Subsystem
Initial Conditions:
  The force due to gravity is constant due to the allocated mass of the robot being 657g.
  One foot is planted while the other is moving, this reduces the effective mass distribution, and thus torque by half per leg.
  The lever arms move at a varying pace, shifted by a small factor depending on starting lever arm position.
  Centripetal force of the legs is negligible due to negligible leg mass.
  The reference for the torque on the motor will be in relation to the first lever arm attached to the motor.

## Slide 38: Power Subsystem
Maximum torque occurs when all lever arms are perpendicular to gravitational acceleration.
  This value is: 213.8 mN-m.
During the rotation of the motor, the force of gravity assists the motor, producing negative (referential) torque

## Slide 39: Power Subsystem
From research, only two 3.3V gearbox motors able to achieve the maximum torque anticipated were the Tamiya 70168 with a 344:1 gear ratio and 72005 with a 197:1 gear ratio.
Tamiya 70168 no load current is 150mA, and full load current, at 221 mN-m is 2.1A.
Tamiya 72005 no load current is 150mA, and full load current, at 235mN-m is 2.7A.
For similar torque, the 72005 has more speed, but significantly more current draw. This provides a serious design consideration, as the dual motor drivers on the 3DoT board are rated at 1.2A continuous and 3A pulsed.
With the assumption that the region between stall torque and no load is linear, a current draw profile for each leg can be extrapolated.
  70168
    Average Current: 862mA
    Peak Current: 2.02A
    Max Speed: 38 RPM
  72005
    Average Current: 1.03A
    Peak Current: 2.47A
    Max Speed: 54 RPM
Selection: Tamiya 70168 due to motor driver current limitations

## Slide 40: Power Subsystem
External battery sizing can be determined from this information. With both legs operating at 852mA average current, the average load current for the external source will be 1524mA.
For one hour of continuous use, the combined external battery capacity must be at least 1500mA-h.
This value is within our allocation of 3000mA for the DC motors under continuous operation.

## Slide 41: Electronics Subsystem

## Slide 42
Mechanical Subsystem
Level II requirements
Foot design [TBD] shall have a surface area of [to be calculated] (Level 2-9, 10)
Foot shall assist with stability.
Foot shall not impede movements
Foot design shall have traction [material friction coefficients test for static and dynamic movement] on the following “Game Appropriate” surfaces: (Level 2-9,10)
Linoleum
Carpet
Tile
Cardboard

## Slide 43
Subsystem Design and Unique Tasks (Planned)
Needed Simulations
Tilt Test
Applying different forces to see how much forces is required to tip over the robot.
Stress Test
To simulate divagations that may occur when certain forces or loads are applied.
Static and Dynamic Test
Dynamic: To control impact of time varying load to structure to ensure performance, quality and safety.
Static: A way to assess the contact and connections between parts
Trade-off Studies
Feet Shape
Calculations will be conducted to determine the best surface area for the feet so the robot can walk statically and dynamically.
Materials
Simulations/ Tests will be ran to conclude the best material for the robot.
Material Under feet
Tests/ Simulations will be ran with different traction material to which will be more efficient for the game.

## Slide 44
Subsystem Design and Unique Tasks (Completed)
Needed Simulations
Tilt Test (Not done via Solidworks)
Trade-Off Studies
Material
(Level 2-3) Aluminum and PLA filaments are the materials we will use.
http://arxterra.com/spring-2016-velociraptor-material-trade-off-study-update/

## Slide 45
Mechanical Subsystem
(Level 2-4)Shall have two leg mechanism, modeled after UCI linkages, supporting mass of robot with 50% margin.
Total Mass goal is ~657g; therefore, legs shall be able to support 985.5g
Level II Requirements [3]
http://www.arxterra.com/spring-2016-velociraptor-project-summary/
http://sites.uci.edu/markplecnik/projects/leg_mechanisms/leg_designs/

## Slide 46
Mechanical Subsystem Design
http://sites.uci.edu/markplecnik/projects/leg_mechanisms/leg_designs/
http://mechanicaldesign101.com/linkage-designs/linkage-animations/

## Slide 47
Mechanical Subsystem Design

## Slide 48
Mechanical Subsystem Design

## Slide 49: Project Status Work Breakdown Structure (WBS)

## Slide 50: Project Status Top Level Schedule
Challenges October
  Tests/Experiments
  Trade-off studies
  3D-Modeling
  Simulations
  CDR Presentation
Reduce build time and errors associated with it

## Slide 51: Project Status System/Subsystem Level Tasks
Allocation of resources
3D-Modeling
PCB production

## Slide 52: Project Status Burn Down and Project Completion
Chart: Project Burn Down 8/25 - 12/15
| 42607 | 42614 | 42621 | 42628 | 42635 | 42642 | 42649 | 42656 | 42663 | 42670 | 42677 | 42684 | 42691 | 42698 | 42705 | 42712 | 42719
Schedule of Tasks | 44 | 44 | 42 | 41 | 40 | 37 | 31 | 17 | 16 | 8 | 6 | 5 | 4 | 4 | 2 | 0 | 0
Tasks To-Do | 44 | 44 | 43 | 42 | 41 | 39
% Completion | 0 | 0 | 1.1364 | 2.2727 | 3.4091 | 5.6818

## Slide 53: Mass Report

## Slide 54: Power Report

## Slide 55: Project Budget:$400.00 ($388.05 Worst Case)
Cost Report |  |  |  |  | 
Resource | Quantity | Expected Cost ($) | Actual Cost ($) | Uncertainty (%) | Margin (±g)
Servo Head/Tail | 1 | 15.00 |  | 25% | 10.00
Servo Body | 1 | 15.00 |  | 25% | 10.00
DC Motors | 2 | 25.00 |  | 25% | 15.00
3DoT Board | 1 | 0.00 |  | 20% | 0.00
Battery/3DoT | 1 | 3.55 |  | 5% | 1.00
Battery External | 4 | 50.00 |  | 30% | 15.00
Battery Charger | 1 | 20.00 |  | 35% | 10.00
PCB Printing Cost | 1 | 30.00 |  |  | 10.00
Frame (PLA Material) | 1 | 40.00 |  | 20% | 20.00
IMU | 1 | 9.00 |  | 5% | 3.00
Hardware (screws/bolts) |  | 10.00 |  | 25% | 2.00
Aluminum Chassis | 1 | 17.00 |  | 5% | 2.00
Motor Drive | 1 | 4.00 |  | 15% | 1.50
Hall Effect Sensor | 2 | 4.00 |  | 15% | 2.00
Shipping |  | 30.00 |  | 50% | 10.00
Project Allocation |  |  |  |  | 400
Total Margin |  |  |  |  | 115.50
Total Expected Cost |  |  |  |  | 272.55
Contingency |  |  |  |  | 242.95